## Slide 1: Advanced ParFlow Short Course CLM Activities
October 3-4, 2019
University of Arizona
This material and short course was supported by the National Science Foundation and Department of Energy
Laura Condon, University of Arizona
Nick Engdahl, Washington State University
Reed Maxwell, Colorado school of Mines

## Slide 2: Common Land Model Activity 1: Finding Variables
Developed by:
Jennifer Jefferson

## Slide 3: Why should you know how to find variables in the CLM code?
Inevitably, someone will ask: “How does the model compute x?”
You want to change how the model computes x
You want to know where a variable from the input file is used

## Slide 4: Where do you search for variables?
pfsimulator – clm folder includes all CLM .F90 modules parflow_lib folder includes solver_richards.c

## Slide 5: How do you search for a variable?
Type in name to search bar in Finder window
Use grep (global regular expression print) command from terminal window
(on a Mac)

## Slide 6: Variations of grep
http://www.gnu.org/software/grep/manual/grep.htm
-l list names of files
-r recursively look through files in a given directory
* wildcard symbol
grep command is very similar on Linux http://www.tecmint.com/12-practical-examples-of-linux-grep-command/
http://www.computerhope.com/unix/ugrep.htm

## Slide 7: Let’s do an example: sand (from drv_vegm.dat)
1. Navigate to director to search in
2. Search for “sand” in Fortan files within the directory

## Slide 8: Example (sand)

## Slide 9: Example (sand)
Variable Name | sand
Description | percent sand in soil
Units | decimal (-)
Global or Local variable | global
Constant or varying? | Constant for each tile, can vary between tiles
CLM Modules | drv_clmini.F90 drv_gridmodule.F90 drv_pout.F90 drv_readvegtf.F90 drv_tilemodule.F90
If/Do statements? | For every soil layer (nlevsoi)
Additional comments | Sand used to compute variables clm%tkmg, clm%csol -> clm_thermalk.F90 -> heat capacity for ground heat flux

## Slide 10: You do: Pick variable(s) you might be interested in, use grep command to find out more information
Vegetation | Ground | Atmosphere
efpot | eflx_evap_soi | forc_hgt_t
eflx_evap_tot | surfalb | hsub
fdry | zsno | displa
qflx_through | csoilc | co2, pco2
seasb | t_soisno | forc_pbot

## Slide 11: You do: Find information about variable(s)
Variable Name | 
Description | 
Units | 
Global or Local variable | 
Constant or varying? | 
CLM Modules | 
If/Do statements? | 
Additional comments | 

## Slide 12: You do: Find information about variable(s)
Variable Name | 
Description | 
Units | 
Global or Local variable | 
Constant or varying? | 
CLM Modules | 
If/Do statements? | 
Additional comments | 

## Slide 13: Tips
Make sure lines are not commented out (!)
Code updates are typically annotated with developers initials, for example:
  RMM = Reed Maxwell
  IMF = Ian Ferguson
  NBE = Nick Engdahl
Be careful of rabbit holes - some variables are more difficult to track down and follow than others
  Find where variable is initialized
  Look at flowchart to see order modules are called

## Slide 14: Common Land Model Activity 2: Testing Single Columns
Developed by:
Jennifer Jefferson
Note: Demo is for operation of PF-CLM from a local version installed on a Mac.

## Slide 15: Why would you want to test CLM with single columns?
Computationally cheaper than whole domain simulation
Can quickly run simulation on laptop
Isolate variable
Obtain information about variable not output (by default) from CLM
Isolate period of time or scenario
Compare effect of change
Clarify computation or conceptual understanding

## Slide 16: Activity 2
Goal: Output and plot 2 variables from CLM
Variables of interest:
clm%btran – vegetation water stress (for transpiration)
taf – canopy air temperature
Both variables are located in clm_leaftem.F90
Neither variable is written out of the model
(demo portion)

## Slide 17: Step 1: Obtain (or locate) files in a folder called “SingleColumnActivity”
Put folder somewhere on your computer, but leave files in this arrangement.

## Slide 18: Step 2: Add print statement to clm_leaftem.F90
Open the file and at the bottom of clm_leaftem.F90 add (will print to …out.txt):
! Update dew accumulation (kg/m2)
clm%h2ocan = max(dble(0.),clm%h2ocan + (clm%qflx_tran_veg-clm%qflx_evap_veg)*clm%dtime)
print*,'111', clm%btran, taf
end subroutine clm_leaftem
Navigate to clm_leaftem.F90

## Slide 19: Tips
Be thoughtful about placement of print statement
  Not in a loop
  Before final value is computed
Select variables strategically so that you can make offline calculations
  To duplicate output
  Think ahead, if possible

## Slide 20: Step 3: Recompile PF-CLM
Open the terminal window
Navigate to pfsimulator folder
cd ...
Recompile code by typing
make install

## Slide 21: Step 4: Run tcl script
Open a new tab in the terminal window (command+t)
Navigate to the “SingleColumnActivity – LW_SC” folder
cd ...
Run tcl script
tclsh LW_SC.tcl

## Slide 22: Step 5: Post-process data
(I used R to load, compare and plot data)
(more moisture, does not limit photosynthesis as much)
(less moisture, limits photosynthesis more)

## Slide 23: Step 5: Post-process data
(air > canopy)
(air < canopy)

## Slide 24: Step 5: Post-process data
Sept.
Oct.
Nov.

## Slide 25: Activity 2
Goal: Run a single column domain and plot variable from single file output
Example single column setup is provided:
.tcl script
(3) CLM files
1D forcing file
  Little Washita, OK
  File begins on September 1, 1998 at 0 GMT
  (7pm CT August 31, 1998)
Pressure file
Restart file
(active portion)

## Slide 26: (Some) Decisions to Make
How many time steps to simulate?
Restart or not?
What CLM variable to plot?
  See end of introduction slides for list and order
set stopt 2184.0
pfset TimingInfo.BaseUnit 1.0
pfset TimingInfo.StartCount 0
pfset TimingInfo.StartTime 0.0
pfset TimingInfo.StopTime $stopt
pfset TimingInfo.DumpInterval 1.0
pfset TimeStep.Type Constant
pfset TimeStep.Value 1.0
#pfset ICPressure.Type HydroStaticPatch
#pfset ICPressure.GeomNames domain
#pfset Geom.domain.ICPressure.Value -1.0
#pfset Geom.domain.ICPressure.RefGeom domain
#pfset Geom.domain.ICPressure.RefPatch z-upper
pfset ICPressure.Type PFBFile
pfset ICPressure.GeomNames domain
pfset Geom.domain.ICPressure.FileName "LW_Loam_SU.out.press.00006.pfb"
pfdist "LW_Loam_SU.out.press.00006.pfb"